## Slide 1
ICT1442 – COMPUTER NETWORKS 1 –
Department of ICT
School Of Education, Humanity
And Social Sciences
EDEN UNIVERSITY

## Slide 2
Optical Fiber Types and Structures

## Slide 3: Optical Fiber Types - Single-Mode
Single-Mode vs. Multimode Fibers
    Optical fibers are thin strands of glass or plastic used to transmit data as light signals over long distances.
    They come in two main types: single-mode and multimode fibers, each with different structures and uses.
Single-Mode Fibers:
Core Diameter:
  Approximately 8-10 micrometers (µm).
  Smaller core size allows only one light mode (or path) to propagate through the fiber.
Wavelength: Typically operates at wavelengths of 1310 nm and 1550 nm, which are optimal for long-distance communication.

## Slide 4: Optical Fiber Types - Single-Mode
Light Propagation:
Light travels in a straight path (single mode), minimizing modal dispersion.
This reduces dispersion and attenuation, which are factors that can degrade the signal over distance.
Low modal dispersion means that signals can travel longer distances without significant distortion or loss.
Distance and Bandwidth:
Capable of transmitting data over long distances, up to 80-100 km without the need for signal boosting.
Supports very high bandwidth, making it ideal for high-speed data transfer.

## Slide 5: Optical Fiber Types - Single-Mode
  Applications:
    Long-distance telecommunication, metropolitan networks, high-speed data transfer, internet backbone, and cable television networks.
Advantages:
  Suitable for long-distance communication.
  High bandwidth capabilities and long-distance transmission.
  Less signal attenuation (signal loss) and dispersion.
Disadvantages:
  More expensive and difficult to splice and connect compared to multimode fibers.

## Slide 6: Optical Fiber Types - Multimode Fibers
Core Diameter:
Larger than single-mode fibers, typically around 50 to 62.5 µm.
Larger core size allows multiple modes (paths) of light to propagate simultaneously.
Light Propagation:
Allows multiple modes or paths of light to propagate or enter the fiber at different angles, hence follow different paths which can cause modal dispersion.
This can lead to a broader pulse as the signal travels, reducing the bandwidth and limiting the distance the signal can travel effectively.
Multiple light modes cause modal dispersion, where different light paths reach the destination at different times.
Modal dispersion limits the distance and bandwidth of the signal.

## Slide 7: Optical Fiber Types - Multimode Fibers
Wavelength:
Operates typically at wavelengths of 850 nm and 1300 nm.
Distance and Bandwidth:
Suitable for shorter distances (up to 2 km) and lower bandwidth applications, such as within a building or on a campus.
Lower bandwidth compared to single-mode fibers, making it ideal for local area networks (LANs) and data centers.
Application:
Used in Local Area Networks (LANs), data centers, and short-distance communication.
Used in short-distance communication, such as within buildings, on campuses.

## Slide 8: Optical Fiber Types - Multimode Fibers
Advantages:
Easier to splice and terminate, making installation and maintenance simpler and cheaper.
Disadvantages:
Limited distance and bandwidth due to modal dispersion.
Structural Differences
Core:
The central part of the fiber where light is transmitted.
Made of highly pure glass or plastic.
Single-mode fibers have a smaller core, whereas multimode fibers have a larger core.

## Slide 9: Optical Fiber Types - Structural Differences
Cladding:
A layer surrounding the core that reflects light back into the core using total internal reflection.
Both types of fibers have cladding with a diameter of around 125 µm.
Typically made of glass with a lower refractive index than the core.
Coating:
A protective outer layer, usually made of plastic, that provides mechanical strength and protection against environmental damage.
It also helps prevent fiber breakage during handling and installation.

## Slide 10: Index Profile – Step & Graded-Index Fibers
The index profile of an optical fiber refers to how the refractive index of the core changes from the center of the core to the cladding.
The two primary types of index profiles are step-index and graded-index.
These profiles significantly impact the way light propagates through the fiber and determine the fiber's performance characteristics.
Step-Index Fibers
Structure:
Core: The core has a uniform refractive index.
Cladding:
The cladding surrounds the core and has a lower refractive index, creating a sharp boundary or step in the refractive index between the core and cladding.

## Slide 11: Index Profile – Step – Index Fibers
Light Propagation:
Light travels in a zigzag path through the core by reflecting off the core-cladding boundary at specific angles.
The sharp refractive index difference causes light rays to undergo total internal reflection, keeping the light within the core.
All light rays take the same path length but travel at different angles, which can cause modal dispersion in multimode step-index fibers.
Types:
Single-mode Step-Index Fiber:
Has a very narrow core that allows only one mode of light to propagate.
It is commonly used for long-distance communication.

## Slide 12: Index Profile – Step – Index Fibers Cont.
Multimode Step-Index Fiber:
Has a larger core that allows multiple light modes to propagate.
It is less common due to higher modal dispersion.
Applications:
Used in applications requiring short to moderate distances, such as in simple data transmission and low-speed communication systems.
Advantages:
Simple design and easier to manufacture.
Cost-effective for basic applications.
Disadvantages:
Higher modal dispersion in multimode step-index fibers, limiting their bandwidth and distance capabilities.

## Slide 13: Graded-Index Fibers
Structure:
Core:
The refractive index of the core gradually decreases from the center towards the cladding in a parabolic or exponential profile.
Cladding:
Surrounds the core and has a uniform refractive index, lower than the outermost part of the core.
Light Propagation:
Light rays follow a curved, sinusoidal path rather than a zigzag path.
The gradual change in the refractive index causes the light rays to bend smoothly as they travel through the core, reducing the amount of modal dispersion.
Different light modes converge at nearly the same time at the output, which increases the fiber's bandwidth and performance.

## Slide 14: Graded-Index Fibers Cont.
Types:
Primarily used in multimode fibers, as the graded-index profile effectively reduces modal dispersion compared to step-index multimode fibers.
Applications:
Commonly used in Local Area Networks (LANs), data centers, and other medium-range communication systems.
Advantages:
Lower modal dispersion compared to step-index multimode fibers, leading to higher bandwidth and longer effective transmission distance.
Disadvantages:
More complex and expensive to manufacture than step-index fibers.

## Slide 15: Comparison: Step-Index vs Graded-Index Fibers
Dispersion:
Step-Index Fibers:
Have higher modal dispersion, especially in multimode configurations, which limits bandwidth and distance.
Graded-Index Fibers:
Reduce modal dispersion significantly, allowing for higher bandwidth and longer distances.
Bandwidth:
Step-Index Fibers:
Limited bandwidth, particularly in multimode fibers, due to the spread of light paths.
Graded-Index Fibers: Higher bandwidth as light paths are more synchronized, reducing pulse broadening.

## Slide 16: Comparison: Step-Index vs Graded-Index Fibers
Applications:
Step-Index Fibers: Suitable for short-distance, low-bandwidth applications or simple communication systems.
Graded-Index Fibers: Preferred for medium-distance, higher-bandwidth applications such as LANs and data centers.
Step-index fibers are simpler and cheaper but are limited in bandwidth and distance due to higher modal dispersion, making them suitable for basic, short-distance applications.
Graded-index fibers are more advanced, offering better performance in terms of bandwidth and distance, making them ideal for medium-range communication systems.

## Slide 17: Fiber Materials and Construction
Optical fibers are constructed from materials that can transmit light efficiently with minimal loss and distortion.
The materials used are critical to the performance, durability, and application of the fibers.
The construction of optical fibers involves multiple layers that protect and enhance the performance of the fiber.
Materials Used in Optical Fibers
Core and Cladding Materials
Silica (Glass) Fibers:
Core Material:
High-purity silica (SiO₂) is the most common material for the core due to its excellent optical properties, including low attenuation and high transmission over a wide range of wavelengths.

## Slide 18: Fiber Materials and Construction Cont.
Cladding Material:
Also made of silica but with a slightly lower refractive index than the core, allowing total internal reflection of light within the core.
Doped Silica:
The refractive index of the core can be adjusted by doping with materials such as germanium dioxide (GeO₂), phosphorous pentoxide (P₂O₅), or boron trioxide (B₂O₃).
Plastic Optical Fibers (POF):
Core Material:
Made from polymethyl methacrylate (PMMA) or other plastics.
Cladding Material:
Often made from a fluorinated polymer with a lower refractive index than the core.

## Slide 19: Fiber Materials and Construction Cont.
Advantages:
Flexible, easy to handle, and cost-effective for short-distance applications.
Disadvantages:
Higher attenuation and lower bandwidth compared to glass fibers.

## Slide 20: Construction of Optical Fibers
Core
Function: The central region of the fiber where light is transmitted.
Materials: High-purity silica for glass fibers; PMMA for plastic fibers.
Design: In single-mode fibers, the core is very small (about 8-10 µm) while in multimode fibers, the core is larger (about 50-62.5 µm).
Cladding
Function: Surrounds the core and has a lower refractive index to ensure total internal reflection, keeping light signals within the core.
Materials: Silica with a different dopant concentration for glass fibers; fluorinated polymers for plastic fibers.
Design: Typically has a uniform diameter of about 125 µm in both single-mode and multimode fibers.

## Slide 21: Construction of Optical Fibers Cont.
Coating
Function: Protects the core and cladding from physical damage, moisture, and other environmental factors.
Also provides mechanical strength and flexibility.
Materials: Made from materials like acrylate or silicone.
Design: Typically consists of multiple layers, including a primary coating that is soft and cushions the fiber, and a secondary coating that is harder for additional protection.
Strength Members
Function: Provide additional mechanical strength and protect the fiber from tensile stresses during installation and operation.
Materials: Often made from materials like aramid yarn (e.g., Kevlar), steel wires, or fiberglass.

## Slide 22: Construction of Optical Fibers Cont.
Design: Incorporated within the fiber cable structure, surrounding the coated fiber.
Outer Jacket
Function: The outermost layer that protects the entire fiber cable from environmental factors such as abrasion, chemicals, and UV light.
Materials: Made from robust materials like polyethylene (PE), polyvinyl chloride (PVC), or other plastics.
Design: Can be designed for specific environmental conditions, such as UV-resistant jackets for outdoor use or flame-retardant jackets for indoor use.

## Slide 23: Types of Optical Fiber Cables
Simplex Fiber Cable:
Contains a single fiber, used for one-way data transmission.
Duplex Fiber Cable:
Contains two fibers, used for two-way data transmission.
Ribbon Fiber Cable:
Contains multiple fibers arranged in a flat ribbon, used for high-density applications.
Loose Tube Cable:
Contains multiple fibers within a gel-filled tube, providing protection against moisture and physical stress.
Tight Buffered Cable:
Each fiber is individually coated with a buffer layer, providing better handling and ease of termination.